## Slide 1: Optics optimization and chromaticity correction in PS2 NMC rings
March 19th, 2007
PS2 meeting
Y. Papaphilippou

## Slide 2: Outline
2
Optimised NMC ring with dispersion supressor
  Refining the straight section matching
Chromaticity correction
  First order
  Second order and chromatic beta beating

## Slide 3: The NMC ring II
Arc module with 1 asymmetric FODO cell with 4 + 3 bends and a low-beta doublet with 4 families of quads, with max. strength of 0.1m-2 and total length of 73m
Suppressing arc dispersion with phase advance close to multiple of 2π and 2 extra quad families
Straight section with 7 FODO cells drift of 9.5m) using 2 matching quadrupoles
Ring of 1346m, with 10 quad families (max strength of 0.1m-2)
  Tunes of (13.8,13.4), γt of 10.9i, chromaticities of -18.7, -29.5
  Max beta of 58m and 56m and min. and max. dispersion of -8.2m and 10.2m
Matching not perfect for horizontal phase advance of 90o in the straights

## Slide 4: Optimizing the arc module
1 symmetric FODO cell with 3 + 3 bends and a low-beta doublet
  Phase advances of 294o,310o per module
  γt of 10.2i
  4 families of quads, with max. strength of 0.1m-2
  Max. beta of 49m and 57m
  Min. dispersion of -2.9m and maximum of 7.5m

## Slide 5: Arc and straight section
Dispersion suppression with 2 extra quad families in the last arc modules
Last arc quad. shared between arc and straight
Straight section with horizontal phase advance of 87.5o
Straight section drift of 10.2m
Only two families of quadrupoles are used
Extra two families can be added for extra internal phase adjustments
Perfectly matched to the arc

## Slide 6: The NMC ring II
  Three types of 8 (+2) quadrupole families (max. strength of 0.1m-2) for a length of 1346.4m
  γt of 11i
  Tunes matched to (14.8,15.2)
  Max. β’s of around 60m both planes
  Dispersion of -2.3m and maximum of 4.6m
  Tunability between 14 and 16 in both planes but penalty on the beta function maxima
  Chromaticities of -21.5, -32.2

## Slide 7: Chromaticity correction
Sextupoles of 0.4m long placed in the low beta doublet
In principle 2 families needed for chromaticity correction
Second-order chromaticity and off-momentum β-beating not corrected
δp/p=-0.5%
δp/p=0.5%

## Slide 8: Next steps
8
Optimise and correct chromaticity in NMC ring I (module with dispersion suppressor)
Optimise sextupole strength and working point for good dynamic aperture
Introduce non-linear correction schemes