## Slide 1: Optics considerations for PS2
February 20, 2008
Dejan Trbojevic, Yannis Papaphilippou, and Ricardo de Maria

## Slide 2: Outline
Introduction: Flexible Momentum Compaction
An example of PS2 racetrack lattice with gt= i 13, with the basic block gt=i 10.4 and zero dis. straight
  Fundamental block gt=i 10.4
  Matching Block
  Zero dispersion straight sections
  1346 meters race-track
Next necessary steps

## Slide 3: Flexible Momentum Compaction Modules
The first publication: D. Trbojevic et. all, “Design Method of High Energy Accelerator Without Transition Crossing”,EPAC 90, Nice, 1536-1538.
I had introduced new
“normalized dispersion” space
with coordinates:
Placing the x vector bellow the vertical axis c makes the momentum compaction ac < 0 the total integral negative:

## Slide 4: Design and optics constraints for PS2 ring are followed
Basic beam parameters | This example required
Injection kinetic energy [GeV] | 4
Extraction kinetic energy [GeV] | ~ 50
Circumference [m] | 1346 1346
Transition energy [GeV] | 13i 10i
Maximum bending field [T] | 1.73 < 1.8
Maximum quadrupole gradient [T/m] | 17.56 < 17
Maximum beta functions [m] | 34.3 < 60
Maximum dispersion function [m] | –2.45 – 2 < 6
Minimum drift space for dipoles [m] | 0.5 0.5
Minimum drift space for quads [m] | 0.45 – 1.6 0.8

## Slide 5: High filling factor FMC
The “high-filling” factor arc module
γt of 10 i
Max. horizontal beta of 32 m and vertical of 34 m
Min. dispersion of –2.45m and maximum of 2 m
Chromaticities of -1.96-1.14
Total length of 59.3 m

## Slide 6: The fundamental block – the arc module
Bd
Bf
Bd
Bf
Bd
Bf
Bd
Bf
Bd
Bd
The combined function dipoles are used to provide better filling factor.
The gradient in the in the focusing bend is GF=+3.993 T/m, while in the defocusing bend is GD=-4.18 T/m
GF3
GD3
GD3
GF3
The gradient in the in the focusing quad is GF=+17.55 T/m, while in the defocusing quad is GD=-14.37 T/m

## Slide 7: The fundamental block – the arc module
Bf
Bd
Bd
Bd
Bd
Bd
Bd
GD3
GF3
GD3
GF3
Bf
Bf
Bf
gt = i 10.47
nx = 0.802 - 4.4 ex +1.9 ey
ny = 0.526 + 1.9 ex +8.1 ey
The sextupole induced tune shift

## Slide 8: The arc block

## Slide 9: Matching block between a single arc cell in the middle and zero dispersion straight section cells at both ends:
The picture shows zero dispersion in the straight section FODO cell

## Slide 10: The matching X-cell to the zero-dispersion straight

## Slide 11: Matching M-cell from X to the basic module in the arcs

## Slide 12: Half of the zero dispersion straight section

## Slide 13: Racetrack PS2 without transition crossing: gt= i 13.1
nx = 16.598 + 70. ex + 59.1 ey
ny = 12.405 + 59.1 ex + 80 ey
The amplitude tune
shift by the sextupoles second order tune shift:
Chromaticities:
xx =-24.1,xy =-16.5, Circumference:
C=1346 m
Maximae of
betatron functions: bx_max=32 m,
by_max =34.3 m,
Dispersion:
-2.45 m < Dx < 2.1 m

## Slide 14: Betatron Functions in the whole ring

## Slide 15: Layout
Racetrack:
Integration into existing/planned complex:
  Beam injected from SPL
  Short transfer to SPS
  Ions from existing complex
All transfer channels in one straight
Minimum number of D suppressors
  High bending filling factor
  Required to reach 50GeV
PS2
SPL
Linac4
PSB
PS

## Slide 16: Summary
This example looks very decent.
Chromaticity correction: second order tune shift induced by sextupoles is very small.
Very good momentum acceptance.
Tunability pretty good.
Dynamical aperture evaluation needs to be finished.
The value of the gt needs small correction. This might raise the maximum dispersion values from Dmax=-2.46 - 2 m to Dmax -2. 7 – 2.3 m.